## Slide 1: MWA Status
L. Greenhill (Harvard/Smithsonian)
RTS/Survey – Proj. Sci.
Digital 6T first light
512T in simulation
Haystack, MIT, SAO, Harvard, Austr. Consort., RRI
MWA-ers also at the workshop:
D. Mitchell, Randall Wayth, Steve Ord (CfA)
Judd Bowman (CIT), Colin Lonsdale (Haystack)
Chris Williams (MIT), Stewart Gleadow (U.Mel)

## Slide 2: Characteristics (thus far)
80-300 MHz
30 MHz BW (instant.)
8000 short dipoles •
  1.2x104 m2 @ 100 MHz
  1.0x104 m2 @ 200 MHz
  2.9x103 m2 @ 300 MHz
512 [4x4] tiles
  131k baselines
full polarization
15 - 45∘ FWHM
768 x 40 kHz channels
  5500 total
  +16 voltage beams
6m - 1.5 km bslns •
  325m for 32T
  16 outriggers (3 km)
  sky noise limited •
  TRX = 30 K @ 200 MHz
  TRX =130 K @ 110 MHz
real-time pipeline dependent •
  8s resolution
40 Gb/s throughput
1000x1000 pxl native
  3x oversampled
  Drty map every 8s
O(10) Tflop/s load •
  GPU accelerated cluster
  64 nodes
  20 kW max
Wide-field large-N hierarchical beamforming array

## Slide 5
8T / 32T
Today

## Slide 6
New generation dipoles
Beamformer
Happy
grass

## Slide 7
Prototype Rack mounted RX

## Slide 8
Correlator Board in Assmebly

## Slide 9
Hydra A
First self-calibrated images via digital RX: 6T Apr/May

## Slide 10: Schedule
06/10
06/09
01/10
01/09
32T
Demo
256T
512T
32 RX ch
fielded
H/W
Correlation
[1 board]
8T
S/W
Correlation
Site visits: monthly until summer;
eng. tests during summer;
32T integration thereafter
Build out

## Slide 11
end