Radio Frequency Interference Mitigation in Pulsar Astronomy
Large Aperture Experiment to Detect the Dark Ages (LEDA)
Jonathon Kocz
CfA
LWA Users Meeting 26th-27th July 2012

---
What are we looking for?
Pritchard & Loeb 10
LEDA
EDGES

---
LEDA Summary
- Demonstrate a large-N correlator
  - A scalable design
- Suppression of systematics in total-power measurement
  - Array-based calibration, ionosphere, gain patters, etc
  - All-sky pulsar calibration of gain patterns
- Discovery of the HI absorption feature to infer the initial conditions of reionization
- Requires:
  - Implementing a full correlation backend for the LWA
  - Generalized package for warped snapshot cal/im
  - Discover HI absorption feature

---
RFI subtraction using a reference antenna.
Outriggers

---
Outriggers
Snapshot array and total power dipoles

---
Outriggers

---
Calibration and Imaging

---
Warped Snapshot

---
CUDA Wide-field Array Processing
(cuWARP: after Mitchell et al. ′08; Ord et al. ′10)
Subtract model visibilities:
FFT distorted sky maps & sample with PB kernels
Calibrator measurements (peeling)
Send one snapshot of visibilities from the database
k=0 (1st calibrator)
RFI detection, flagging, etc.
Update calibrator model and adjust visibility subtraction
Measure ionospheric distortions
Phase to calibrator k & average in time and freq.
k++ (next
calibrator)
Measure Jones matrices
Stream through the visibility dataset generating calibration models and residual sky maps.
The residual maps, along with updated calibrator information, are used to update the sky model.
The whole process is repeated, using the updated sky and calibration models, until the residual images have converged.
at convergence
Grid residual visibilities
apply cal. using PB kernels)
Update wide-field calibration parameters
Primary beam parameters
2D ionospheric phase screens
FFT to form warped images
Resample images
remove ionospheric &
wide-field distortions
Integrate images in time
Snapshot (residual) imaging pipeline

---
Polarized Point Source/ISM
Δθ ~ 15′
FOV = 2400 °2
190 MHz / 31 MHz
ΔRM = 1 rad m-2
-50 < RM < 50 rad m-2
(Bernardi , LG, et al. 12)

---
Pulsar Calibration
LOFAR LBA Data:
• 30-90 MHz

---
Correlator

---
Correlator

---
Correlator - Final
FPGA:
16 x ROACH2s
2 x 16-input ADCs
(512 inputs total)
Performs:
PFB (4096 channels)
Channel Selection (2400 channels)
10GbE packetisation
RFI detection/excision
CPU:
2 x 10GbE inputs
Receiving 19.2+ Gb/s
Performs:
Data capture
Data unpacking
(10000100 →
10000000,
01000000)
Pulsar break out
GPU:
2 x GPU
Read 38.4+ Gb/s
Performs:
Cross-correlation
Averages defined number
of outputs
CPU:
Additional averaging
Writes data to disk

---
Correlator - Current
FPGA:
4 x ROACH1
2 x 4-input ADCs
(32 inputs total)
Performs:
PFB (4096 channels)
Channel Selection (1628 channels)
10GbE packetisation
CPU:
2 x 10GbE inputs
Receiving 11 Gb/s
Performs:
Data capture
Data unpacking
(10000100 →
10000000,
01000000)
GPU:
2 x GPU
Read 22 Gb/s
Performs:
Cross-correlation
Averages defined number
of outputs
CPU:
Additional averaging
Writes data to disk

---
Correlator
- Current status:
  - Two 32-input complete correlator designs have undergone bench testing:
    4096 selectable channel F-engine → PSRDADA → Harvard X-engine
    2048 channel F-engine → #PIPE → Harvard X-engine
  - LEDA-64 correlator on ROACH2 under development.
https://github.com/GPU-correlators/xGPU

---
Deployment Schedule:
- RFI testing LEDA-32 prototype (next week)
- Deployment LEDA-32 Mid-August
- Deployment LEDA-64 2012
- Deployment LEDA-512 2013

---
– END –